# Design For Testability
In this chapter, general idea of Design for Testability philosophy is presented. IEEE standards regarding testing are also described in brief.
## Testing in production engineering

In modern electronics, testing has become a crucial issue of every production line. Detecting potential faults during manufacturing may save a lot of effort and reduce overall production costs, according to the Pay more now and pay less later rule. Good test should give an unequivocal answer whether the design works properly and what kind of error (stuck at 1, stuck at 0, short or bridge [Wil]) was detected. Two main attributes of testing are: [DFT]

- Controlability – ability to control the tested unit in order to set the desired input sequence;
- Observability – ability to observe unit's output signals in order to gather the output data.

Many approaches to measuring controlability and observability of a given design are currently in use. The most popular one is the Sandia Controllability Observability Analysis Program method, also known as SCOAP. This method uses integers to describe difficulty of controlling and observing internal nodes of a system. The higher the number, the harder it is to observe the considered node.

## Moreover, good testing environment should be universal and fast enough to test many components at once. In an ideal situation all the nodes are controllable.
## Design for Testability

Design for Testability (DFT) is a method of circuit design that enhances the design with special testing functionalities and enables forming test scan chains out of units under test (UUTs). In every unit, an additional piece of hardware is required to perform nothing but tests.

Testing according to the DFT guidelines provides a response vector which is later being compared with a response vector coming from a properly functioning device. As a result, it is possible to both define and locate faults within the tested unit. Obviously, test vectors must be chosen carefully to provide a full diagnostic functionality. Apart from ad hoc testing by using test points within the design, two main methods are used: scan chains and built-in scan tests. It is possible to mix DFT-compliant functionalities together i.e. as presented in [Dat]. The most popular methods are described below.

//tu jakieś metody optyczne. Będzie fajnie - NP
## Built-in Scan Test

It is possible to implement a simple and quick DFT-compliant internal test which is used by an unit to test itself. Such mechanism is called a Built-in Scan Test (BIST) and its functional diagram is shown on Fig. XX.

Fig. XX Example functional diagram of a built-in scan test. Source: [Ana]

Three main functional blocks may be distinguished as presented in [Cec]:

- Pattern generator that uses a stored or pseudo-random pattern;
- Signature analyzer that stores unit's response;
- BIST controller that activates the test and analyzes the response.

As a result, the unit itself may decide whether it works properly. Such test may be programmable, or involve testing memories used in the design [Ncu]. It may also run automatically when powering up the device as so-called Power On Self Test (POST).

## Scan-chain Test

Scan-chain testing is a sequential DFT-compliant technique that allows to test many daisy-chained ICs simultaneously as presented on Fig. XX. It is widely used in testing electronic components. There are even approaches to tailor this technique to test 3D integrated circuits [Cse]. Naturally, more than one scan chain may be put under test at once.

Fig. XX Scan-chained units under test. Source: [Cre]

In Scan-chain test, testing path leads through all the tested components. Automatic Test Pattern Generator (ATPG) is used to generate an input sequence which is being shifted in to a special test input of the first component. Output sequence is shifted out on a special test output of the last one. Special pin that triggers the test and clock signal are also required. Such transmission must be synchronous to gather a proper output vector.

The main application of a scan chain is a Boundary Scan Path present in IEEE 1149.1 standard.

# IEEE standards regarding scan test

To meet the market requirements, IEEE standards regarding testing are still developed. In this chapter, IEEE standards regarding boundary scan tests will be presented and described in brief. The main standard will be further explained in next chapter

## Role of the JTAG group

JTAG is an abbreviation of a Joint Test Action Group (previously the Joint European Test Action Group). It was formed in middle 80s by a group of engineers from various companies that decided to form an universal standard regarding debugging and testing electrical components. The first result was the IEEE 1149.1 standard commonly known as JTAG introduced in 1990.
JTAG is a special serial interface added to a chip that consists of four or five pins. In order to test many electrical component, they require to be daisy-chained, unless several scan chains are used. The main point of the JTAG norm was board-level testing of both components and their interconnection. This is done by using a 5-pin or 4-pin interface connected to the Test Access Port that controls the data flow. Standard JTAG architecture is shown in Fig. XX.

Fig. XX Standard JTAG architecture introduced in IEEE 1149.1. Source: [Embe]

 Nowadays, its application range includes debugging embedded systems that uses JTAG as a communication interface. There is also a possibility to use JTAG to write software and data into NOR and NAND Flash memory.

## JTAG-related IEEE standards

The main JTAG standard has been extended into various related standards regarding tests of some specific components. The main standards derived from IEEE 1149.1 are: IEEE 1149.4, IEEE 1149.6, IEEE 1149.7 and IEEE 1150. Each of these standards doesn't replace JTAG, but supplies it with some specific functionality, depending of what kind of integrated circuits is to be tested.
## IEEE 1149.4 standard

The 1149.4 standard was introduced in order to enable measuring analog components placed on printed circuit boards. General block diagram of the 1149.4 standard is shown in Fig. XX.

Fig. XX Block diagram of a mixed-signal IEEE 1149.4 structure. Source: [Sun]

 In this standard, analog pins are handled: two extra pins, AT1 and AT2, are added to the interface. Generally, AT1 pin is stated to be used as a stimulus, whereas AT2 pin is used to capture response of a circuit. These pins act independently from other four/five TAP pins. They may be connected to parallel low-frequency analog test buses as well as to the analog pins of the tested integrated circuits. One design may contain various analog test buses for different frequency ranges or accepted voltage levels.

## IEEE 1149.6 standard

IEEE 1149.6 standard is a boundary scan standard prepared for advanced digital networks and devices making use of low-voltage differential signaling (LVDS). The general functionality enhancement is shown in Fig.XX.

Fig.XX LVDS support introduced in IEEE 1149.6. Source: [Jta]

It was developed to test AC-coupled signals which are denoted by placing a coupling capacitor between driver and receiver as shown on Fig. XX. In such circuit, signal passing through the capacitor decays over time. This extension wasn't considered in the basic IEEE 1149.1 functionality. A new instruction called AC-EXTEST is added to the instruction register to send and save data pulses. Any fault may be identified by analysing the pulse response of the tested device.

Fig.XX Coupling capacitor placed between driver and receiver. Source: [Agi]

This standard is also enriched with possibility of using AC test pattern generator.

## IEEE 1149.7 standard

IEEE 1149.7 (aka Compact JTAG or cJTAG) is a a complementary enhancement of the 1149.1 standard. It is known as standard for reduced pin and enhanced functionality TAP and overall boundary scan architecture. This standard was ratified by IEEE in December 2009. Main differences between IEEE 1149.1 and 1149.7 are shown in Tab. XX.

Tab.XX Main differences between JTAG and cJTAG standards.

Property	IEEE 1149.1 - JTAG	IEEE 1149.7 - cJTAG
Power consumption	Only one ON state.	Four selectable power modes used to reduce power consumption and enable low-power devices
Accessing a specific device	Available only by setting other devices into BYPASS state	Individual device addressing and system-level bypass that shorten the length of a scan chain
Topology	Standard (serial)	Star topology with simplified physical connection of the devices
Number of pins	Four or five: TDI, TDO, TMS, TCK and TRST (optional)	Reduced to two: TMS and TCK

Idea of a chip-level bypass introduced in IEEE 1149.7 is shown in Fig. XX.

Fig. XX Concept of a scan-level chain with and without bypass. Source: [Cor]

## IEEE 1150 standard

IEEE 1150 is a separate JTAG standard derived from IEEE 1149.x standards family. Its application is a bit different- it concerns testing embedded cores with System on Chip (SoC) functionality and their associated circuitry. This standard enriches IEEE 1149.1 with many new, FPGA-specific features. Parallel test access mechanisms (TAM) are introduced. New way of describing units under test is also developed: Boundary Scan Description Language is being replaced by a Core Test Language (CTL) whose main purpose is to faciliate interoperability and cooperation between various entities. General description of the Core Test Language functionality is shown in Fig. XX.

Fig. XX Schematic idea of Core Test Language applications. Source: [Ctl]

This standard is still under development by 1450.6.2 IEEE group.

## IEEE 1532 standard

IEEE 1532 standard stands for Boundary-Scan-based In System Configuration (ISC) of Programmable Devices. The In System Configuration term means that there exists a possibility of programming the specified devices after they have been located on the board. It is already used in some chips by Altera from the MAX family [EET]. This standard introduces a new feature called an „in-system configuration”. This feature enables simultaneous programming of standard-compliant devices mounted on a PCB what would reduce overall programming time. Every such component would be possible to reconfigure, verify or erase its content, despite its vendor and despite its vintage [Spr]. The main purpose of so-called concurrent programming would be to significantly improve programming time efficiency: there would be no need to use special procedures just to reprogram the device. Therefore, IEEE 1532-compliant BSDL files are enhanced with algorithmic information used for automatic configuration of tested devices [Ste]. System state machine has become equipped in 4 new modes, apart from 2 states available in IEEE 1149.1 (System and Test) : Unprogrammed, ISC Accessed, ISC Complete and Operational. 1532 standard system state machine is shown on Fig. XX.

Fig. XX System state machine of the IEEE P1532 standard. Source: [IEP]

Moreover, instruction set has changed drastically. Instead of instructions known from IEEE 1149.1, there are four new ISC_xxx mandatory instructions in Test Access Port (ISC_ENABLE, ISC_PROGRAM, ISC_DISABLE and ISC_NOOP) and many optional ones that support additional access procedures (i.e. ISC_DISCHARGE, ISC_PROGRAM_DONE, ISC_ERASE_DONE, ISC_DATA_SHIFT, ISC_ADDRESS_SHITF etc.). As a result, device behaviour is well-defined before, during and after programming and it is theoretically impossible to induce any unexpected behavior that could damage other mounted components. Security mechanisms are also introduced by a special ISC_PROGRAM_SECURITY mode.

# IEEE JTAG standard

This chapter describes detailed functionality of the IEEE 1149.1 JTAG standard and its auxiliary mechanisms, such as Instruction/Data registers and Test Access Port. It is fully based on the IEEE 1149.1-2001 standard. Example test patterns are also presented.
## JTAG test circuitry

In IEEE 1149.1, a special model of test logic was defined. Such model should make use of 4 or 5 I/O signals: input data TDI, output data TDO, clock TCK, test mode select TMS and optional reset TRST. IEEE-compliant model included three crucial components:

- Test Access Port – a logic block allowing to control instruction and data registers by a finite state machine set by the TMS input pin;
- Instruction Register – latched shift register that can be serially loaded with the instruction selecting the performed test;
- Data Register – set of various shift-register based circuits. One of these registers (or even its part) is selected to be linked between TDI and TDO pins, basing on current instruction latched onto the instruction register. Example of a generic data register is shown in Fig. XX.

Fig. XX IEEE-compliant test data register. Source: [MAU]

What is important, some TAP actions take place on rising edge of TCK, whereas other actions are performed on its falling edge.

## Test Access Port

The main task of the Test Access Port is to define which operation is actually performed. It includes a TMS pin-driven finite state machine which allows to control both instruction and data registers. All possible states and transitions between them are presented in Fig.XX.

Fig. XX Test Access Port controller state diagram. Transitions between adjacent states depend on the value of the TMS signal. Source: [IEE].

Remarkably, all the IR-marked states concern instruction register operations, while all DR-marked states concern data register operations. Due to control faciliating, both registers-related state transitions are symmetric. All the transitions should take place on a rising edge of TCK, whereas test logic actions may occur either on rising or falling edge of TCK.

The most important states are Reset, Shift and Update states – other states may be considered temporary, i.e.the Pause state is used only to halt temporarily the shifting process. Exact role of each TAP state is described in Tab. XX.

Tab.XX Description of Test Access Port states.

State	Role	Edge [rising/falling]	Remarks
Test-Logic Reset	Test Access Port reset state		Achievable by setting the TRST pin or within 5 clock cycles by passing from any other state when TRST is not used.
Run-Test/Idle	Test Access Port Idle state
Select-XX-Scan	Selects whether next state will regard Instruction or Data Registers
Capture	?????????????????????
Shift	Shifts bits serially from TDI to TDO
Exit1	Exit from Capture or Shift state		Lasts for 1 clock cycle
Pause	Halts current operation
Exit2	Exit from Pause state		Lasts for 1 clock cycle
Update	Updates shadow registers with values from either data or instruction register

# REFERENCES
[Wil] http://www.wiley.com/legacy/wileychi/mblin/supp/student/LN16DesignforTestability.pdf
[DFT] http://www.asic.co.in/ppt/DFTnew.pdf
[Dat] http://www.date-conference.com/proceedings/PAPERS/1998/DATE98/PDFFILES/03D_3.PDF
[Ana] http://www.analog.com/library/analogDialogue/archives/42-02/bist.html
[Cec] http://web.cecs.pdx.edu/~ecex75/pdf/BIST_Tut1.pdf
[Cse]http://www.cse.psu.edu/~yuanxie/Papers/ICCD2007-3D.pdf
[Cre] http://www.corelis.com/education/Tips_DFT_Considerations_Boundary_Scan_Chain.htm
[Ncu] http://www.ee.ncu.edu.tw/~jfli/memtest/lecture/ch04.pdf
[Cor] http://www.corelis.com/whitepapers/Major-Benefits-of-IEEE-1149.7.pdf
[Sun] http://grouper.ieee.org/groups/1149/4/Sunter_1149.4_Tutorial.pdf
[Agi] http://www.home.agilent.com/en/pd-1730771-pn-E1196A/ieee-11496-boundary-scan?&cc=PL&lc=eng
[Jta] http://www.jtag.com/en/content/ieee-11496
[Embe] http://www.embecosm.com/appnotes/ean5/html/ch02s01s02.html
[Ctl] http://grouper.ieee.org/groups/1500/itc00/ctl.pdf
[EET] http://www.eetimes.com/document.asp?doc_id=1128318
[Spr] http://link.springer.com/chapter/10.1007%2F978-1-4615-0367-5_9#page-2
[Ste] http://www.dateconference.com/proceedings/PAPERS/2004/DATE04/PDFFILES/09C.PDF
[IEP] http://grouper.ieee.org/groups/1532/p1532.PDF
[MAU] (co to było :P)
[IEE] (norma IEEE 1149.1)