Vendor-specific programming interfaces

1149.1-compliant JTAG requires 4 or 5 pins to function properly. It may be a bottleneck when considering microprocessors in smaller packages or simplicity of the transmission – in example, if one requires merely a simple Flash programmer for a low-cost devices family, there is no point in implementing whole robust JTAG interface. Some companies such as Texas Instruments overcame this problem by introducing a reduced pin count JTAG standard (aforementioned IEEE 1149.7) [Chi]. TI's cJTAG IP core is claimed to be the very first semiconductor solution having the standard implemented- even its name stands for “Compact JTAG”. Finally, 1149.7 was ratified in late 2009. Naturally, 1149.7 standard did not replace 1149.1 in full. Potential risks of such replacement are well described in [IPE].

Various vendors introduced their own JTAG-like protocols used to debug or program processors with reduced pin count. Therefore ARM introduced SWD, Atmel introduced PDI and DebugWIRE for 8-bit processors with limited resources[Mik]. Even Texas Instruments developed its own Spy-Bi-Wire protocol used to program MSP430 devices [MSP]. Usually, in such devices both 1149.1 JTAG and vendor-specific interfaces are enabled. A special procedure of switching between the protocols and the default protocol is also described. Sometimes large piece of vendor-specific protocols is protected by NDA and not all functionalities are available to users.

In a typical vendor-specific protocol one pin is used as a clock signal, whereas the second one is a bi-directional data bus with the following generic configuration:

- Pin acts as a transmitter when data are sent to the processor;
- Pin acts as a receiver when acknowledge signals, ID codes or read memory values are sent by the processor.

Example of an interface of Atmel XMEGA AVR devices family that make use both of a default JTAG and a vendor-specific interface is shown on Fig.XX.

Fig. XX Example interface supporting both JTAG and vendor-specific interface. Source: [Equ]

Two popular vendor-specific programming interfaces, SWD and PDI, are described and compared below. Description of the SWD interface is based on its implementation in STM32F4xxxx family, whereas description of PDI interface is based on its implementation in AVR1612.

SWD programming interface

SWD term is an abbreviation of Serial Wire Debug. This serial interface provides an alternative to atypical JTAG interface in ARM processors family. It was introduced with the Cortex-M family [Cor] and finally specified in [AD5]. Some Cortex-M based MCUs support only SWD interface.
Core of the appropriate ARM processors integrates both Serial Wire and JTAG debug ports. Both interfaces make use of the same pins.

SWD makes use of only two pins from the JTAG interface: TMS becomes its Serial Wire Data IO (SWDIO) and TCK becomes its serial wire clock (SWCK). By default, JTAG port is active. To switch from JTAG to SW-DP, a special sequence of bits described in [STM] must be sent on the TMS pin while TCK pin is active. Sometimes an additional trace output TRACESWO pin is used to access the Serial Wire Viewer.

SWD interface allows read and write operations on both DPACC and APACC banks of registers. All bits are transmitted LSB-first. Each transaction via the interface consists of three phases:

1. A 8-bit long packet request is transmitted by the host via SWDIO. Packet requests defines whether DP or AP registers are accessed, whether the read or write operation is requested. It also includes address field of the register and a parity bit.
2. Target transmits an acknowledge response. SWD uses the same acknowledge values as JTAG-DP (OK and WAIT) and introduces a new FAULT acknowledge.
3. Target or host transmits 32 bits of write/read data + an additional single parity bit.
  [TODO] Zastąpić te 3 punkty grafiką, za mało obrazków w tym rozdziale!!!
Since Cortex-M3 family, SWD interface is equipped with an auxiliary CoreSight debugger block. This block enables variety of debugging possibilities, i.e.Serial Wire Viewer macrocell that provides possibility of real-time data tracing by SWD pins. As a result, the following data become traceable [EPr]:
- Program counter;
- Read/write data cycles;
- I/O port states;
- Variable values;
- Input and output ports of interrupt handling routines;
- Event counters;
- Data about single instruction execution time.
All of the data above may be visualized in Keil Microvision Logic Analyzer[SWV].

PDI programming interface

PDI is an abbreviation of Program and Debug Interface. It supports high-speed programming of all species of non-volatile memory as well as on-chip debugging. It requires two pins and an additional VCC/GND connection between the programmer and the device. Mandatory pins are:

- PDI_CLK: clock input acting as a reset pin;
- PDI_DATA: data input and output pin acting as a test pin.

PDI physical interface is serial and it uses a standard UART frame format as shown on Fig.XX.

Fig.XX UART frame format used in PDI interface. Source: [APD]

PDI may be either in transmit or receive mode. By default, it is in receive mode and waits for a start bit. Input data are sampled on a rising edge of PDI_CLK.

PDI must be enabled before it is used. As in SWD interface, a special sequence must be sent on PDI_DATA and PDI_CLK pins. In case of PDI, this section is much simpler and it consists of setting PDI_DATA high for a period longer than the equivalent external reset minimum pulse width. An additional process is required to get access to non-volatile memories and their controller for programming. User must send a correct 64-bit wide NVM key in the PDI while choosing the KEY instruction. PDI interface is automatically disabled if there is no activity on the PDI_CLK line for approximately 100 μs.

Control of PDI is made by a small set of its own 8-bit long commands. Most of these commands define an operation (load or store data) and applied mode of addressing (indirect or direct). Additional information about address size or pointer access are required when respectively direct or indirect addressing is used. Programming instructions enable a wide range of operations such as chip erase, reading the non-volatile memory, loading/erasing page buffer or loading/erasing application section. CRC value of Flash memory and application section are accessible too. Moreover, even boot loader and calibration sections may be accessed.

References

[Chi] http://chipdesignmag.com/display.php?articleId=2668
[IPE]http://blogs.ip-extreme.com/2010/03/myth-busted-ieee-11497-does-not-replace-ieee-11491.html
[MIK] http://www.mikrocontroller.net/articles/DebugWIRE
[MSP] Texas Instruments, MSP430™ Programming Via the JTAG Interface:User's Guide, SLAU320M.
[Equ] http://www.equinox-tech.com/products/details.asp?ID=1429
[Cor] http://www.support.code-red-tech.com/CodeRedWiki/HardwareDebugConnections
[AD5] ARM Debug Interface v5
[STM] STM32xx manual
[Epr] Paweł Adamczyk, Serial Wire Viewer:„Śledzenie” ARM-ów w realu, Elektronika Praktyczna 2/2009, s.124-127.
[SWV] Robert Boys, Serial Wire Viewer (SWV) for ARM Cortex-M3 Processors ARM Real-Time Trace aids debugging, Version 2.1, ARM, Ltd.
[APD] AVR1612: PDI programming driver